## Slide 1: Designing Nature-Based “Migration” Projects in Face of Uncertainties
Stuart Siegel, PhD, PWS
San Francisco Bay National Estuarine Research Reserve
siegel@sfsu.edu
Presentation at the Wetland Migration Workshop
September 18, 2023

## Slide 2: Design Foundation
Why are we pursuing wetland migration?
To maintain wetland functions over the long term in the face of environmental change
To utilize a valuable function: capacity for natural systems to benefit people (e.g., “nature based strategies”)

## Slide 3
Steep
slope
Levee/
Hard
Shoreline
Sea
Level
Rise
T2
T1
Gentle slope
Estuarine Transgression
Ample opportunity
Limited opportunity
Very minor opportunity
Migration Type 1: Horizontal
Notes: Last key strategy = allowing for marshes to migrate landward, aka Transgression
Works well where land slopes are gentle –
Common around the Delta
Some available around Suisun
Lower estuary very limited to non-existent
  Developed shorelines
  Steeper shorelines
  San Pablo Bay has some potential
  Maybe some potential in South Bay but mostly developed

## Slide 4
Sea Level Rise (cm/century)
52
100
180
Suspended Sediment Concentration (mg/L)
25
100
Schile et al. 2014
Migration Type 2: Vertical (winner: SLR or accretion?)






Notes: Putting time, SLR scenarios, and SSC scenarios together paints a range of outcomes, China Camp illustrated. Which path we follow remains to be seen, and perhaps we can do something about some parts of this equation.

## Slide 5
Vegetation depth & salinity
H
M
L
S B F
Tidal Salt Marsh
Tidal Freshwater
Marsh
Tidal Brackish Marsh (fresher)
Tidal Brackish Marsh (saltier)
Migration: Estuarine Location Matters
Notes: Relevant to maintaining marsh elevations and reversing subsidence in restored marshes
Relevant to sediment trapping and retention capacities
5

## Slide 6: Design Foundation: Core Uncertainties of Change
How fast the changes will arrive
How big the changes will be
How many changes we will have to contend with
How our actions and inactions will promote or ameliorate these changes
How interactions amongst these changes and with societal actions may play out

## Slide 7
Clean Water Act Section 401
Porter-Cologne Water Quality Control Act
McAteer-Petris Act
Fish and Game Code
California Endangered Species Act
Federal Endangered Species Act
National Historic Preservation Act
Migratory Bird Treaty Act
California Environmental Quality Act
National Environmental Policy Act
Rivers and Harbors Act
Delta Reform Act
Suisun Marsh Protection Act
Clean Water Act Section 402
Clean Water Act Section 404
Clean Water Act Section 303(d)
Title 23
33 USC Section 408
Magnussen-Stevens Act
State Leases and Encroachment
Federal Navigation
State Agencies: BCDC, RWQCB, CDFW, DSC, SLC, SHPO, CVFPB, Caltrans
Federal Agencies: USFWS, NMFS, USACE, USEPA, USCG
Design Foundation: Projects Require Permits!!

## Slide 8: Project Design Overarching Approach
Look forward as far as viable, follow natural examples, integrate techniques, understand place and people. Then design projects with the greatest likelihood of natural processes maintaining functions over the long term.
Local Natural Examples
Applied in Local Project Designs

## Slide 9: Hydrogeomorphic Settings Drive Design
Tidal edge: open bay (wind fetch, water depth), large tidal slough (currents), smaller tidal slough, watershed connection
Upland edge: steepness; levee or infrastructure; managed (e.g., agriculture) or natural
Marsh/former bayland type: tidal ancient, centennial, older restoration, new(er) restoration, diked subsided bayland (elevation, width, veg type)
Tidal flood protection: natural edge (none needed), integrated (eg levee), segment (not protecting stand alone)
Sediment supply: bay (low, med, high), watershed

## Slide 10
Goat Island Marsh
Lower Spring Branch Creek
Suisun Hill Hollow
Three Restoration Projects
Lower Spring Branch Creek (built 2019)
Seasonal stream flows into First Mallard Slough
15-acre tidal marsh restoration
Reconnected 14 floodplain acres and 1 mile of edge to wetland migration
Suisun Hill Hollow (built 2019)
Seasonal stream flows into Goat Island Marsh (currently diked)
8-acre seasonal wetland restoration
Goat Island Marsh (final design starting)
80-acre tidal marsh restoration
4,200-ft natural upland transition
Will connect to Suisun Hill Hollow
Figure 3
Restoration Projects Location Map
Tidal marsh
Diked marsh
Seasonal drainages
Rush Ranch: Natural Edges, Seasonal Streams

## Slide 11
Tidal marsh
Seasonal floodplain
Muted tidal marsh
Two 3.5’ open culverts
“L-shaped” berm
Lower Spring Branch Creek: Before Restoration

## Slide 12
Old ranch road,
two 3.5’ culverts
First Mallard Slough (tidal)
Lower Spring Branch Creek (muted)
Tidal reconnection via arch culvert
Lower Spring Branch Creek Restoration (2019)
Goal: reconnect floodplain to tidal marsh
Replace two 3.5’ culverts with one large arch culvert – full tidal connectivity, SLR accommodation
1,200’ of new tidal channel – tidal circulation
Lower an old berm – create high marsh
Lower ranch road – allow storm overflow
First Mallard Slough Tidal Marsh
Lower Spring Branch Creek
Upper Spring Branch Creek
Rush Ranch SF Bay NERR
Linking Habitats Across the Landscape

## Slide 13: Sonoma Creek: Centennial Marsh, Levee at Upland
Limited or no transition habitat or high tide refuge
Drowned marsh interior and levee toe: little/no veg, breeds mosquitoes
Low ability for habitats and resident organisms to adapt to stressors (e.g., climate change and SLR)

## Slide 14: Design Elements
Use of multiple design elements
Central channel to drain interior excess ponding
Lateral channel to drain swales along levee toe
Marsh mounds for high tide refuge
Marsh-upland transition ramp
Flood tide asymmetry (natural bayfront berm) + high sediment load = impeded direct bay connection, may limit channel longevity (SLR could help!).
Central Channel
Lateral Channel
Transition Ramp
Marsh Mounds

## Slide 15: Design: Very Gentle Sloped Transition Ramp
2018
2015

## Slide 16
North Habitat Levee
West Levee
North levee: tidal flood control, habitat levee
Levee pannes
West levee: separates Sonoma Baylands
Dredge ponds
Marsh mounds
Restoration Project Design
Notes: Do we want to add an animation to call out the mounds (arrow, inset photo) to highlight the issue that the re-veg components were not completed (leads into the problem statement)?

## Slide 17
Oct 2015 (pre-breach)
July 2019 (3.75 yr tidal)
scarp
Western levee
Omitted: Vegetate < Breach. Result: Erosion
July 2021 (4.75 yr tidal)
Oct 2016 (1 yr tidal)
scarp
Northern levee

## Slide 18: The Fix: Multi-Element Nature-Based Ecotone Rebuild
Schematic: Peter Baye (2019)
Physical elements: scarp grading, LWD installation, vegetation planting, dried bay mud placement, gravel armor and toe berm placement, brush fence
Process elements: tidal redistribution and vegetation colonization of placed mud (into swash bars) and gravel (into “beaches”), continued accretion of full site

## Slide 19
Gravel Toe Berm
Brush Fence
Bay Mud
Gravel Toe Berm
Brush Fence
Logs
Bay Mud
Brush Fence
Gravel lag armor (below mud)
Brush Fence, Toe Berm, Lag Armor, Bay Mud

## Slide 20: Nature-Based Shoreline Erosion Protection Works!
July 2021
August 2023

## Slide 21
Stuart Siegel, Feb 2016
Opportunity: natural edge
Constraints:
Highway 37
Lakeville Highway
Rail line
Result:
Restore 1,000 acres south of rail line only
Zero natural edge
Diked Baylands
Below Sea Level
Cougar Mountain
(Sears Point Raceway over hill to the north)
Lakeville Hwy
Hwy 37
Rail line
Area restored in 2015 to tidal marsh
Timing is Everything!!
Notes: Note that Roger will get into what did get done along the rail line edge

## Slide 22: Think Boldly! Thank you
siegel@sfsu.edu